## Slide 2: Lecture 4: Intro to Computer Architecture

## Slide 3: The Uber Stack
Applications |  |  | 
Middleware |  |  | 
Operating Systems |  |  | 
Computers |  |  | 
Processors | Memories | Display Components | Interconnects
Materials |  |  | 
Physics |  |  | 
H
A
R D W A R E
S O F T WA R E
Notes: Fed from developments in lowest and highest levels
Even if you don’t remember the past, you are condemned to repeat it…
What is the cycle time?

## Slide 4: How We Interact with Computers
Applications
Operating System
Hardware
User

## Slide 5: Digital Components

## Slide 6: “Digital”
DIGITAL - Digital means discrete.
Digital representation is comprised of a limited number of data points to encode information.
Most of our electronic devices use Digital techniques to work with data and information
Since we have a limited number of data points to work with, it means that many representations are approximations of the real thing

## Slide 7: Analog vs. Digital
Analog is continuous, Digital is discrete

## Slide 8: The difference between “analog” and “digital”
ANALOG
DIGITAL

## Slide 9: Analog vs Digital
Discrete Digital Sampling of an Analog Event

## Slide 10: Bits ( = Binary Digits)
Internally, all data in a digital device is contained in memory locations that are either on or off.
Thus everything in memory can be thought of as being expressed in “bits”, aka “binary digits”
where on = 1 and off = 0
a single “bit” can represent only 2 values,
0 or 1

## Slide 11: Binary numbers
Obviously with 1 bit we can only represent two values 0 and 1
With 2 bits we can represent four different values:
00, 01, 10, 11
With 8 bits (otherwise known as a byte) we can represent 256 values
( 0-255)

## Slide 12: Nomenclature
A BIT is a single 1 / 0 position
A NIBBLE is 4 BITS
A BYTE is 8 BITS
A WORD is a multiple of BYTES eg: 16 bits, 32 bits, 48 bits, 64bits……….
Common nomenclature today is to define memory storage and data capacity in BYTES

## Slide 13: More Nomenclature
As computers have become capable of processing and storing more data, we have coined:
KiloBytes (Thousands)
MegaBytes (Millions)
GigaBytes (Billions)
TeraBytes (Trillions) –Library of Congress 30Tb
PetaByte (1000 Trillion)
ExaByte (Million Trillion)

## Slide 14: Base 2 (Binary) vs. Decimal Comparison
105 104 103 102 101 100
10n = 100,000 10,000 1000 100 10 1
27 26 25 24 23 22 21 20
2n = 128 64 32 16 8 4 2 1

## Slide 15: Representing Data in the Computer
Internally, everything--data, programs, text, you name it--is represented in bits.
With an array of bits, we can represent any number or, thru assignment, any character so, for example:
0011 0000 = decimal 48 = “H”
(256 combinations, 0 to 255)

## Slide 16: How could we represent letters for instance?
For characters we need 26 letters, 10 numbers, special marks, etc. About 127 possibilities including upper and lower case and special control characters
Unicode is an agreed upon code in which every character, numbers, etc. is given a unique 8 bit code (1 byte).
So we need 4 bytes to represent the word “love”

## Slide 17: Remember, everything is represented in bits!
2 Bits – 00, 01, 10, 11
3 Bits –
4 Bits-
.
.
8 Bits-
16 Bits-
24 Bits-
4 values
8 values
16 values
256 Values
65,536 Values
16,777,216 Values

## Slide 18: Good tutorial on Binary
http://www.swansontec.com/binary.html

## Slide 19: What are computers made of?
Primarily Transistors
Invented in 1951, the Transistor is the basic electrical building block for all modern electronics
“the greatest invention of the 20th century”
For Digital applications, transistors are packaged in what is known as Integrated Circuits (ICs) aka “CHIPS”
As many as 30+ Billion Transistors can be packaged in a single large IC today

## Slide 20: Anatomy of a Transistor
Transistors are fabricated using purified silicon (derived from quartz) and tiny amounts of impurities such as selenium or gallium arsenide to create what is called a “semiconductor”
Semiconductors allow us to control the flow of electrical charge (electrons) very precisely.
Billions of semiconductors can be placed on an integrated circuit using a process called photolithography

## Slide 21: Transistor Functionality
In various circuits Transistors can be made to:
Amplify or Attenuate electrical signals
Invert electrical signals
Store electrical voltage values
Switch electrical signals off and on
Transistors can be interconnected to create logic circuits commonly known as “GATES”

## Slide 22: Simple Silicon Semiconductor Devices

## Slide 23: Intel 4004 Processor Chip circa 1971
It could only add and subtract 4 bits at a time.

## Slide 24: AMD Athlon64 Processor

## Slide 25: Use of Logic Gates in Computers
Primary Uses:
Switches and logic circuits that can be switched between 0 and 5 volts. In this way a Switch can signify a “bit” that is a 1 or a 0
Storage of voltage levels equivalent to 0 or 5 volts. In this way a “bits” of memory can be implemented or pixels on an LCD display on a laptop can be created

## Slide 26: AND and OR Gates

## Slide 27: By combining gates we can create useful functions such as a the ability to store a bit of information
The purpose of a latch is to allow a data value to be stored temporarily. So that we can hold it and “use” it for awhile…like a “bit” of memory

## Slide 28: The Von Neumann Machine
CPU = Central Processing Unit
Memory
INPUT
OUTPUT

## Slide 29: A Typical PC CPU Board

## Slide 30: Fetch, Decode, Execute Cycle
Computer instructions are stored (as bits) in memory. To run a program, each instruction is:
Fetched from memory.
Decoded (the computer figures out what it should do based on the number).
Then the instruction is executed.
The speed at which this cycle occurs is determined
by the system clock

## Slide 31: Cycle Times
Generally the faster your computer can get through a fetch-decode-execute cycle, the faster it will perform.
Cycle times are measured in “gigahertz”, a billion cycles per second.
PCs these days reach 3500 Megahertz or 3.5 Gigahertz (3 billion cycles/sec)

## Slide 32: Memory
Each memory unit has its own address
Memory units are organized in groups of Bytes (8 bits) or Words (16, 24, 32, 64 or 128 bits)
0 1 2 3 4 …………………………………..16 Billion
0
1
1
1
0
0
0
1

## Slide 33: Random Access Memory
The main computer memory is called RAM (Random Access Memory)
It is “random” in that one may access any addressable memory unit independently of any other (and thus in “random” order).
In almost all modern machines the smallest single addressable amount of memory is one byte.
Memory is measured in megabytes or gigabytes or terabytes (millions, billions or trillions)

## Slide 34: RAM chips on a Circuit board

## Slide 35: Dynamic Random Access Memory
RAM allows for both reading and writing in memory. Contrast this with ROM (read-only memory).
Most RAM is volatile, or “dynamic”. When you turn off the power, the contents of RAM is lost.
Sometimes one talks about DRAM which is short for dynamic RAM).

## Slide 36: Read Only Memory
Read Only Memory can only be read from
It’s contents cannot be altered or written over easily
This type of memory is used to hold instructions that need to always be there
For example, the initial instructions that are executed when your PC is turned on which instructs the machine to load Windows from the disk drive

## Slide 37: Central Processing Unit
manages the instruction-execution cycle
FETCH – DECODE – EXECUTE
coordinates the activities of other devices

## Slide 38: Machine Language
Every computer CPU has its machine language, the set of basic instructions it knows how to execute.
A typical set of instructions might mean, “get the contents of certain a memory locations and put it in the accumulator register and then add them together and store the results in a different memory location”

## Slide 39: Machine Instructions
Such an instruction would consist of two numbers:
One would be the address of memory to be accessed.
The other would be the operation code of the instruction - the (somewhat arbitrary) number that refers to a unique and particular type of instruction

## Slide 40: Structure of Instructions
Op code
Memory address
Suppose we used 32 bits to encode a machine language instruction.
7 bits
25 bits
7 bits would allow us to have 128 different op codes.
25 bits would allow about 32 megabytes of addressable memory. We might need to fetch more bytes if we had to address a larger range of memory

## Slide 41: Information Transfer inside the CPU
Individual bits in a memory unit are transferred to the CPU in parallel (all at the same time).
This is opposed to serially (one at at time).
The same goes for information transferred between registers in the CPU.
A 64 bit machine can transfer 64 bits in parallel.

## Slide 42: Central Processing Unit
manages the instruction-execution cycle
FETCH – DECODE – EXECUTE
coordinates the activities of other devices

## Slide 46: Types of Processor Operations
Data Movement Operations
  moving data from memory to the CPU
  moving data from memory to memory
  input and output
Program Control
  starting a program
  halting a program
  skipping to other instructions
  testing data to decide whether to skip over some instructions
Arithmetic and Logical Operations
  integer arithmetic
  comparing two quantities
  shifting, rotating bits in a quantity
  testing, comparing, and converting bits

## Slide 47: Challenges to Continuation of Moore’s Law
The thickness (in atoms) between the silicon layers in transistors is getting very thin as we attempt to cram more transistors into the same amount of space…so much so that new materials need to be developed
HEAT!! As we put more and more transistors on a chip, the ability to cool it and keep it from burning up is increasingly a problem
Noise - As more transistors are packed ever more tightly together, the noise level of the circuits increases which affects reliability

## Slide 48: Quad Core Processor
4 CPUs on one chip….. One way to increase performance…
Parallel Processing!

## Slide 49: Smaller, Cheaper, Faster!
The Mantra of the Semiconductor Industry

## Slide 50: A New Computing Paradigm?
Quantum Computing
Seeks to use the “spin” of atomic particles to implement digital systems
Molecular computing
Using molecules to hold electrical charges instead of using transistors
Both very much in primary research….not here yet

## Slide 51: Questions?